Arm 7 structure - ARM Cortex M4

Cortex M4 series is used STM32F446RE circuit.

        ------------------------------------------------------------

Generating triggers for external components external devices (Harddisk, Circuit, etc.. like that many)

GPIO Pin,GIPO Pin = in Circust (That Ping)

For 1 port = 16 Pins

Total 8 port (PortA to Port H)

1 Pins= Multiplexing

   Eg :(GPIO, GPOI,UART, etc..)

It Can be use other process in 1 pins.

   Eg: In clg he is student, in home for mom he is son.

High Z state - It connot be Calculated (cannot come crt value 1 or 0 ).

Use Pull Up Resistor or Pull Down Resistor down to gets Value (1=1, 0=0).

For 1 = use Pull up
      0 = use Pull down.

To get the value.

For I2C use 2 pull up for OPEN DRAIN.

2 1 = 2

2 2 = 4

210 = 1024=1 kilo

1024 = 1 kilo

Circuit Code Eg in Day 1 code.

RCC -> AHBIENR

OR OPERATOR [Bitwise] | = ((1<<28)) [ // “ | ” = OR OPERATOR [Bitwise] symbol ]
      replace 0 into 1 for 28 position or pin to turn on led or do input process.

#define Por-EEN EC (Any name)
       (some code inbtw)

        (1<<0)

modular register = tell them go to in input or output mode.

for 1 Pin = 2 Pins asigned.

ODR = Output Data Register.

ODR = Tells them to OUTPUT (or) INPUT mode.

MEMORY MAP : HEXADECIMAL

 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F

 Hexadecimal notation uses digits 0-9 and letters A-F to represent values from 0 to 15.

        4- GIGA Bits. (calculation in class)

Hexadecimal (4 bit) -> 16(24)

0 - 0000

1 - 0001

2 - 0010

3 - 0011

4 - 0100

5 - 0101

6 - 0110

7 - 0111

8 - 1000

9 - 1001

A – 1010

B - 1011

C – 1100
D -1101

E-1110

F – 1111

( written like in 0xA = 10 [for eg] “x” = Hexadecimal )

Decimal 10: In hexadecimal, it is represented as A.
Decimal 255: In hexadecimal, it is represented as FF.
Decimal 1000: In hexadecimal, it is represented as 3E8.
Decimal 12345: In hexadecimal, it is represented as 3039.
Decimal 65535: In hexadecimal, it is represented as FFFF.
Decimal 42: In hexadecimal, it is represented as 2A.